This call queries the mode (attribute) of the specified file.
##### Syntax
DosQFileMode (FilePathName, CurrentAttribute, Reserved)
##### Parameters
;FilePathName (PSZ) - input : Address of the file path name. :DosQSysInfo is called by an application during initialization to determine the maximum path length allowed by OS/2. ;CurrentAttribute (PUSHORT) - output : Address of the file's current attribute. 'Bit Description' 15-6 Reserved. 5 File archive 4 Subdirectory 3 Reserved 2 System file 1 Hidden file 0 Read only file These bits can be set individually or in combination. For example, an attribute value of 0021H (bits 5 and 0 set to 1) indicates a read-only file that is archived. ; Reserved (ULONG) - input : Reserved must be set to zero.
##### Return Code
rc (USHORT) - return Return code descriptions are: * 0 NO_ERROR * 2 ERROR_FILE_NOT_FOUND * 3 ERROR_PATH_NOT_FOUND * 26 ERROR_NOT_DOS_DISK * 87 ERROR_INVALID_PARAMETER * 108 ERROR_DRIVE_LOCKED * 206 ERROR_FILENAME_EXCED_RANGE
##### Remarks
The “Volume Label” type attribute is not returned by DosQFileMode. DosQFSInfo may be used for this purpose.
##### Example Code
#### C Binding
<PRE> #define INCL_DOSFILEMGR
USHORT rc = DosQFileMode(FilePathName, CurrentAttribute, Reserved);
PSZ FilePathName; /* File path name */ PUSHORT CurrentAttribute; /* Data area (returned) */ ULONG 0; /* Reserved (must be zero) */
USHORT rc; /* return code */ </PRE>
#### MASM Binding
<PRE> EXTRN DosQFileMode:FAR INCL_DOSFILEMGR EQU 1
PUSH@ ASCIIZ FilePathName ;File path name PUSH@ WORD CurrentAttribute ;Data area (returned) PUSH DWORD 0 ;Reserved (must be zero) CALL DosQFileMode
Returns WORD </PRE>
# Note
Text based on http://www.edm2.com/index.php/DosQFileMode
Family API
DOS	Process Manager	DosBeep DosExit DosSleep DosExecPgm
File Manager	DosChDir DosChgFilePtr DosClose DosDelete DosDupHandle DosMkDir DosMove DosQCurDir DosQCurDisk DosSetFileMode DosOpen DosQFileInfo DosRead DosQFileMode DosQFSInfo DosQVerify DosRmDir DosSelectDisk DosFindClose DosFindFirst DosFindNext DosSetFileInfo DosSetVerify DosWrite DosFileLocks DosSetFHandState DosNewSize DosBufReset DosQFHandState DosSetFSinfo
Memory Manager	DosFreeSeg DosSubAlloc DosSubFree DosSubSet DosAllocHuge DosAllocSeg DosReallocHuge DosReallocSeg DosGetHugeShift DosCreateCSAlias
NLS	DosCaseMap DosGetCtryInfo DosGetDBCSEv DosSetCtryCode DosGetCollate DosGetMessage DosInsMessage DosPutMessage
Date and Time	DosSetDateTime DosGetDateTime
Devices	DosDevConfig DosDevIOCtl DosDevIOCtl2
Signals	DosHoldSignal DosSetSigHandler
Misc	BadDynLink DosGetEnv DosGetMachineMode DosGetVersion DosError DosErrClass DosSetVec
KBD		KbdCharIn KbdFlushBuffer KbdGetStatus KbdSetStatus KbdStringIn KbdPeek
VIO		VioGetBuf VioGetConfig VioGetCurPos VioGetCurType VioGetPhysBuf VioReadCellStr VioReadCharStr VioScrollUp VioScrollDn VioScrollLf VioScrollRt VioScrUnLock VioSetCurPos VioSetCurType VioSetMode VioGetMode VioShowBuf VioWrtCellStr VioWrtCharStr VioWrtCharStrAtt VioWrtNAttr VioWrtNCell VioWrtNChar VioWrtTTY VioScrLock VioPopUp
Tools		BIND
Modules		DOSCALLS.DLL VIOCALLS.DLL KBDCALLS.DLL MSG.DLL
Libraries		API.LIB OS2386.LIB FAPI.LIB DOSCALLS.LIB SUBCALLS.LIB