### KbdSetStatus
Bindings:
C:
typedef struct _KBDINFO { /* kbst */ USHORT cb; /* length in bytes of this structure */ USHORT fsMask; /* bit mask of functions to be altered */ USHORT chTurnAround; /* define TurnAround character */ USHORT fsInterim; /* interim character flags */ USHORT fsState; /* shift states */ }KBDINFO; #define INCL_KBD USHORT rc = KbdSetStatus(Structure, KbdHandle); PKBDINFO Structure; /* Data structure */ HKBD KbdHandle; /* Keyboard Handle */ USHORT rc; /* return code */

MASM
KBDINFO struc kbst_cb dw ? ;length in bytes of this structure kbst_fsMask dw ? ;bit mask of functions to be altered kbst_chTurnAround dw ? ;define TurnAround character kbst_fsInterim dw ? ;interim character flags kbst_fsState dw ? ;shift states KBDINFO ends EXTRN KbdSetStatus:FAR INCL_KBD EQU 1 PUSH@ OTHER Structure ;Data structure PUSH WORD KbdHandle ;Keyboard Handle CALL KbdSetStatus

This call sets the characteristics of the keyboard.
KbdSetStatus (StatData, KbdHandle)
StatData (PKBDINFO) - input Address of the keyboard status structure:
length (USHORT) Length, in bytes, of this data structure, including length.
10	Only valid value.

sysstate (USHORT) The system state altered by this call. If bits 0 and 1 are off, the echo state of the system is not altered. If bits 2 and 3 are off, the binary and ASCII state of the system is not altered. If bits 0 and 1 are on, or if bits 2 and 3 are on, the function returns an error. If binary mode is set, echo is ignored.
Bit	Description
15-9	Reserved, set to zero
8	Shift return is on
7	Length of the turn-around character (meaningful only if bit 6 is on).
6	Turn-around character is modified
5	Interim character flags are modified
4	Shift state is modified
3	ASCII mode is on
2	Binary mode is on
1	Echo off
0	Echo on

turnchardef (USHORT) Definition of the turn-around character. In ASCII and extended-ASCII format, the turn-around character is defined as the carriage return. In ASCII format only, the turn-around character is defined in the low-order byte.
intcharflag (USHORT) Interim character flags:
Bit	Description
15-8	NLS shift state.
7	Interim character flag is on
6	Reserved, set to zero
5	Application requested immediate conversion
4-0	Reserved, set to zero

shiftstate (USHORT) Shift state.
Bit	Description
15	SysReq key down
14	CapsLock key down
13	NumLock key down
12	ScrollLock key down
11	Right Alt key down
10	Right Ctrl key down
9	Left Alt key down
8	Left Ctrl key down
7	Insert on
6	CapsLock on
5	NumLock on
4	ScrollLock on
3	Either Alt key down
2	Either Ctrl key down
1	Left Shift key down
0	Right Shift key down

KbdHandle (HKBD) - input Default keyboard or the logical keyboard.
rc (USHORT) - return Return code descriptions are:
0	NO_ERROR
376	ERROR_KBD_INVALID_LENGTH
377	ERROR_KBD_INVALID_ECHO_MASK
378	ERROR_KBD_INVALID_INPUT_MASK
439	ERROR_KBD_INVALID_HANDLE
445	ERROR_KBD_FOCUS_REQUIRED
447	ERROR_KBD_KEYBOARD_BUSY
464	ERROR_KBD_DETACHED
504	ERROR_KBD_EXTENDED_SG

Remarks
Shift return (bit 8 in sysstate) must be disabled in ASCII mode.
KbdSetStatus is ignored for a Vio-windowed application.
Family API Considerations
Some options operate differently in the DOS mode than in the OS/2 mode. Therefore, the following restrictions apply to KbdSetStatus when coding in the DOS mode:
- KbdSetStatus does not accept a bit mask of 10 (ASCII on, Echo Off).
- Raw (binary) Mode and Echo On are not supported and return an error if requested.
- KbdHandle is ignored.
- Interim character is not supported.
- Turnaround character is not supported.